## Slide 1: CE801
Chandra Naveen Kumar
2003246

## Slide 2: PID Controller
Using two separate PID controllers. One controlling the linear or forward speed and the other controls the steering angle.
INPUTS:
1) Min Right distance to right edge(b/w ranges 379 to 699)
2) the position where min distance was found
The linear speed control PID works on distance error alone but the PID controller which controls the Steering takes both min distance from position for error calculation.
Parameters:
Distance PID
kp_d = 0.05
ki_d = 0.00000001
kd_d = 0.05
Steering PID
kp_a = 0.3
ki_a = 0.000001
kd_a = 0.25

## Slide 3
Right Edge fuzzy Controller
Using two sensor values Right front distance and Right back distance
Instead of using a single value a range of values are used for finding the min distance
Ranges:
Right Front Range : 390 to 540
Right Back Range : 541 to 719
Using 4 labels
2near : 0.0 to 1.0
Near : 0.5 to 1.5
Med : 1.0 to 2.0
Far : 1.5 & beyond

## Slide 4: Rule BASE

## Slide 5: Output membership functions
3 Labels
Turn Right : -1.2 to -0.4
Correction : -0.4 to 0.35
Turn Left : 0.35 to 0.45
3 Labels
Slow : 0.25 to 0.5
Med : 0.3 to 0.5
Fast : 0.45 to 0.75

## Slide 6: Steering control Surface

## Slide 7: Forward Speed Surface

## Slide 8: Obstacle avoidance fuzzy controller
Using three sensor values Front Right distance, Front center distance and Front left distance
Instead of using a single value a range of values are used for finding the min distance
Ranges:
Front Right Range : 670 to 700
Front Center Range : 701 to 19
Front Left Range : 20 to 50
Using 3 labels
Near : 0 to 1
Med : 0.5 to 1.5
Far : 1 & beyond

## Slide 9: Rule base

## Slide 10: Output Variables
3 Labels
Turn Right : -1.8 to 0.0
Correction : -0.5 to 0.5
Turn Left : 0.0 to 1.8
3 Labels
Slow : 0.3 to 0.4
Med : 0.4 to 0.5
Fast : 0.5 to 0.6

## Slide 11: Steering control surface

## Slide 12: Forward Speed Control Surface

## Slide 13: Fuzzy Coordination
1.0
0.5
1.0
Front Obstacle Distance
Firing Strength
Used front obstacle distance for determining the firing strength of each behavior
When there is no obstacle present and the path is clear robot tries to find a right edge and follow it.

## Slide 14: Thank you